## Slide 1
Future US Land Imaging Jeffrey Masek, NASA GSFC
NASA Agency Update – CEOS LSI-VC-2
July 20-22, 2016
Dave Jarrett, NASA HQ
Jeff Masek, NASA GSFC
Harmonized Landsat/Sentinel-2 (HLS) Update
Jeff Masek, Junchang Ju, Eric Vermote, NASA GSFC
Martin Claverie, Jean-Claude Roger, Sergii Skakun, University of Maryland
Jennifer Dungan, NASA ARC
LCLUC - April 14 2017

## Slide 2: Harmonized Landsat Sentinel-2 (HLS) Project
Merging Sentinel-2 and Landsat data streams can provide 2-3 day global coverage
Goal is “seamless” near-daily 30m surface reflectance record including atmospheric corrections, spectral and BRDF adjustments, regridding
Project initiated as collaboration among GSFC, UMD, NASA Ames

## Slide 3: HLS Test Sites
North America: 95
Alaska / NW Canada: 16
South America: 28
South-Africa: 166
Tanzania: 121
Germany: 62
Europe: 15
(w/o Germ.)
Africa: 6 (w/o SA and TZ)
S Asia: 122
NE Asia: 11
SE Australia: 141
69 Test sites (45 from MuSLI team)
783 MGRS tiles
>7.5 million sq. km2
Landsat-8 data set: 147k products From Mar-2013 to Dec-2016
Sentinel-2 data set: 47k products From Jun-2015 to Dec-2016
Online Request Form
https://hls.gsfc.nasa.gov/ test-sites/propose-a-new-site/

## Slide 5: HLS Algorithms overview and status
Atmospheric Correction
BRDF Adjustment
S10 (MSI SR 10m)
S30
(MSI NBAR 30m)
L30
(OLI SR 30m)
M30
(5-day composite NBAR)
Landsat-8 (L1T)
Temporal Compositing
Geographic registration
Geometric Resampling
Sentinel-2 (L1C)
Offset
coefficients
BRDF Adjustment
Geometric Resampling
Band Pass Adjustment
Atmospheric Correction
Algorithm | Current (V1.2) | Other Options
Geographic registration | AROP (Gao et al. 2009, JARS) | -
Atmospheric Correction | OLI and MSI: Landsat-8 6S algorithm | CNES MACCS
Cloud/Shadow Mask | OLI: Landsat-8 6S algorithm output MSI: BU MSI Fmask | CNES MACCS
BRDF Adjustment | Fixed BRDF (Roy et al. 2016, RSE) | Downscaling MODIS BRDF + Fixed BRDF as Backup
Band Pass Adjustment | Fixed, per-band linear regression | Regression-tree (based on spectral shape)
Temporal Compositing | TBD | -

## Slide 6
Mis-registration between Landsat and Sentinel-2
  Up to 35m mismatch due to some areas of relatively poor Landsat ground control (Storey et al, 2016, RSE)
    Magnitude of problem varies around the globe
  USGS will improve Landsat ground control in ~2018-19
  For now, users can use automated cross-correlation algorithms to co-register and/or resample L8 to S2.
Mis-registration among early Sentinel-2
  S2a data (processed before June 2016) showed relative misregistration between adjacent orbits
  Error in yaw payload processing
  Corrected with Sentinel-2 v2.04 processing
HLS uses a single Sentinel-2 image as reference for each time series & AROP to co-register (see next slide)
S2 / L8 Registration Issues

## Slide 7
HLS Circular Error (CE) relative to S2a reference granule

## Slide 8
Grassland
Alfalfa
+
Sentinel-2 Landsat-8
Harmonized Landsat / Sentinel-2 Products
Laramie County, WY
NDVI
Day of Year
mowing
3km
May 4, 2016 (S2)
Aug 8 (L8)
Aug 17 (L8)
Sep 1 (S2)
Oct 20 (L8)
0.1 NDVI 0.9
Seasonal phenology (greening) for natural grassland (blue line) and irrigated alfalfa fields (red line) near Cheyenne Wyoming observed from Harmonized Landsat/Sentinel-2 data products. The high temporal density of observations allows individual mowing events to be detected within alfalfa fields. HLS Products available from https://hls.gsfc.nasa.gov

## Slide 9
Time series of a 3x3 pixel window around the cross
Coordinates: 43.68°N, 1.25°E
Location: South-West France
ρ NIR band
ρ Red band
NDVI
HLS from Sentinel-2A MSI
HLS from Landsat-8 OLI
0 NDVI 1
1.2km
Daily interpolated NDVI
Harmonized Landsat / Sentinel-2 Products
SW France

## Slide 10
55
Schuyler,
Nebraska
USDA 2016 Cropscape
5km

## Slide 11
Schuyler,
Nebraska
HLS NDVI
Filtered, interpolated to daily time step
0.0
1.0

## Slide 12: Websites and Public Interface
HLS website
https://hls.gsfc.nasa.gov
Public access
Sample data available (via FTP)
Algorithm & Product descriptions
NEX project page
https://nex.nasa.gov/nex/projects/1371
Registered user access
All HLS data available
Documents (slides, user guides)

## Slide 13
Reflectance comparison with daily MODIS CMG
  dataset & granule level metric
    evaluation not validation
  up to 5-day window w/ MODIS
  eliminate HLS granules with high number of discrepant 0.05° CMG reflectance values
Per-tile time series smoothness
Per-pixel QA attributes
  Cloud, shadow, water, adjacent cloud (L30 only)
  Inherited L1 QA metadata
HLS QA\QC Processes

## Slide 14: HLS QC: MODIS CMG Comparison
L30
S30
MODIS CMG Reflectance
Discarded S30 Tiles (<3%) due to S2 Cloud Omission

## Slide 15: HLS QC: MODIS CMG Comparison

## Slide 16: HLS QC: MODIS CMG Comparison

## Slide 17: HLS QC: Temporal Smoothness
day
VI (y)
Noise
Approach based on variance among cloud-free VI triplets (Vermote et al., 2009)
Per-pixel metric calculated from median of all triplets (N>6) in time series

## Slide 18: HLS QC: Temporal Smoothness
-> Noisy
Smooth <-
Tile
34HBK
(S.Af)
Tile
31TCJ
(France)
Adding S2 data increases time series noise due to cloud commission

## Slide 19: HLS QC: Temporal Smoothness
Tile
34HBK
Tile
31TCJ
Per-pixel filtering for temporal “outliers” reduces variance
After Filtering
-> Noisy
Smooth <-

## Slide 20: HLS Releases
V1.2 Released February, 2017
  Per-pixel view angle correction
  All bands used for aerosol retrieval
  Fix of pixel indexing problem in v1.1 arising from atmospheric correction, resulting in mis-alignment of 10, 20, and 60m bands
  Registration of all imagery to single reference S2 L1C image
  Correction of bug in Fmask
Known Issues
  Cloud mask for Sentinel-2 needs improvement
    L1C cloud mask poor, difficult to use (vector)
    Fmask better but errors of omission are common
      Boston U. working on improvements
  Atmospheric Correction lags behind LaSRC for L8
    Blockiness & pin-hole drop outs
    Artifacts in snow-covered scenes
  Bug in BRDF implemention (~1% relative error)

## Slide 21: Known Issues
Error in atmospheric correction over snow?
Number of non-cloud, non-shadow observations => water is called shadow

## Slide 22: Future Directions
Version 1.3 – release ASAP to fix minor BRDF bug, add user-requested test sites
Q3-Q4 2017: North America wall-to-wall
  Fully automated processing w/ ~5-day latency
    <24 hours Landsat (USGS/NEX), <2 days for S2 (Google)
    2-10 days for ancillary (ozone, water vapor)
  Leverage AWS for processing, archive, distribution
2018: extension to MuSLI Round 2 sites

## Slide 23
Backup

## Slide 24: HLS Products Specification
S10
Spatial: 10m, 20m, 60m
Spectral Bands: All MSI
Temporal: All Sentinel-2 L1C granules
NBAR: No
S30
Spatial: 30m
Spectral Bands: OLI-like + MSI Red Edge
Temporal: All Sentinel-2 L1C granules
NBAR: Yes
L30
Spatial: 30m
Spectral Bands: All OLI
Temporal: All Landsat-8 L1T granules
NBAR: Yes
M30
Spatial: 30m
Spectral Bands: OLI-like + MSI Red Edge + TIRS TOA
Temporal: 5-day “best pixel” based on min AOT
NBAR: Yes
All 4 products are aligned on the S2 Tiling system (Military Grid Reference System), following UTM zones + 3 letters defining a grid
Tiles are 110km square with 10km overlap for same UTM zone adjacent tiles
109,080m
UTM zone 35
UTM zone 36
Overlap area
S2 Tiles system

## Slide 25: HLS QC: MODIS CMG Comparison